## Slide 1: An introduction to gpu computing and cuda architecture
罗汉杰，机器人组，CVTE中央研究院

## Slide 2: motivation

## Slide 3: motivation
Image quality computation
Image quality computation
Image quality computation
Image quality computation
Image quality computation
Exposure
prediction
Exposure
control
Exposure
Notes: 预计18个月会将芯片的性能提高一倍。
Power=number of cores; Power = (frequency)3

## Slide 4: motivation
Chart: Average Elapsed Time of Different Code Version per Frame
OpenCV CPU version | 24.72
OpenCV GPU version | 19.15
Objective | 10
Notes: 预计18个月会将芯片的性能提高一倍。
Power=number of cores; Power = (frequency)3

## Slide 5
GPU Architecture
CUDA Programming Model
Case Study: Matrix transpose

## Slide 6: GPU Architecture

## Slide 7
“If you were plowing a field, which would you rather use: Two strong oxen or 1024 chickens?”
Seymour Cray
Notes: 西摩·克雷（Seymour Cray），1958年设计建造了世界上第一台基于晶体管的超级计算机。

## Slide 8: Getting PERFORMANCE
Increase processor speed
  Moore's law doesn't hold anymore
  Power scales as frequency
Parallel executing
Notes: 预计18个月会将芯片的性能提高一倍。
Power=number of cores; Power = (frequency)3

## Slide 9: gpu vs cpu
CPU GPU
Notes: Global memory

## Slide 10: gpu vs cpu
CPU
Low compute density
Complex control logic
Large caches
Low latency tolerance
Optimized for serial operations
GPU
High computer density
High data-parallel, throughput(150GB/s VS 25GB/s)
High computations per memory access
High Latency Tolerance
Built for parallel operations
Notes: 强于预测执行，乱序执行
减少每个线程内的延迟（核等待数据的时间）
吞吐量

## Slide 11: gpu vs cpu
CPU architecture attempts to minimize latency within each thread
GPU architecture hides latency with computation from other thread warps
Notes: 强于预测执行，乱序执行
减少每个线程内的延迟（核等待数据的时间）

## Slide 12: GPU Architecture
Streaming Multiprocessors (SMs)
  Perform the actual computations
  Each SM has its own: Control units, registers, execution pipelines, caches
Notes: 940mx , 3 sms , 128 cuda cores

## Slide 13: Canonical execution flow
Copy data from CPU memory to GPU memory
Launch kernel on GPU
Execute kernel on GPU
Copy data from GPU memory to CPU memory
Notes: Global memory

## Slide 14: CUDA PROGRAMMING MODEL

## Slide 15: Thread hierarchy
Thread: Sequential execution unit
  All threads execute same sequential program
Threads Block: a group of threads
    Threads execute in parallel
  Executes on a single Streaming Multiprocessor (SM)
  Threads within a block can cooperate
    Light-weight synchronization
    Data exchange
Grid: a collection of thread blocks
  Thread blocks of a grid execute across multiple SMs
  Thread blocks do not synchronize with each other
  Communication between blocks is expensive

## Slide 16: Thread hierarchy
A thread blocks is run on a single SM
The GPU is responsible for allocating the blocks to the SMs
All the SMs run in parallel and independently
An SM may run more than on block
CUDA make few guarantees about when and where thread blocks will run
Independent execution of blocks provides scalability
  Blocks can be distributed across any number of SMs

## Slide 17: CUDA Kernels
A kernel is executed by many threads
  A kernel is a simple C program
  Each thread has it own ID
  Thousands of threads execute same kernel

## Slide 18: CUDA Kernels

## Slide 19: Memory hierarchy
Three types of memory in the graphic card:
  Global memory: 4GB
  Shared memory: 16 KB
  Registers: 16 KB
Latency:
  Global memory: 400-600 cycles
  Shared memory: a few cycles
  Register: Fast
Purpose:
  Global memory: IO for grid
  Shared memory: thread collaboration
  Registers: thread space
Fast
slow

## Slide 20: CASE STUDY: matrix transpose

## Slide 21: serial
Matrix transpose:
  Size: N*N
But wait... GPU computing is about massive parallelism!

## Slide 22: Performance
Method | Time | Bandwidth
Serial | 466ms | 0.1%

## Slide 23: parallel per row
Parallel per row
Instead of executing transpose_serial() once, execute N times in parallel
1 blocks, N thread per block
transpose_serial<<<1, 1>>>
transpose_parallel_per_row<<<1, N >>>

## Slide 24: Performance
Method | Time | Bandwidth
Serial | 466ms | 0.1%
Parallel per row | 4.7ms | 4.5%

## Slide 25: Parallel per element

## Slide 26: Performance
Method | Time | Bandwidth
Serial | 466ms | 0.1%
Parallel per row | 4.7ms | 4.5%
Parallel per element | 0.67ms | 17.1%
Most GPU codes are memory limited!
Notes: 内存不能及时将数据传递到SM中，或及时存储运算结果，GPU工作工作效率会大打折扣

## Slide 27: Coalescing
Coalescing: GPU is always accessing global memory/DRAM in petty large chunks, 32 or 128 bytes at a time
Notes: [,kəʊə'les]

## Slide 28: SHARED MEMORY

## Slide 29: Performance
Method | Time | Bandwidth
Serial | 466ms | 0.1%
Parallel per row | 4.7ms | 4.5%
Parallel per element | 0.67ms | 31.1%
Shared memory | 0.33ms | 17.1%
Notes: 内存不能及时将数据传递到SM中，或及时存储运算结果，GPU工作工作效率会大打折扣

## Slide 30: Reduce average delay
More threads in the block, more time on average they spend waiting.
We have 32*32=1024 threads each block, each threads doing little work, and waiting until all other threads get done!
Reduce the number of threads per block.

## Slide 31: Performance
Method | Time | Bandwidth
Serial | 466ms | 0.1%
Parallel per row | 4.7ms | 4.5%
Parallel per element | 0.67ms | 31.1%
Shared memory(K=32) | 0.33ms | 17.1%
Shared memory(k=16) | 0.13ms | 43.5%
Notes: 内存不能及时将数据传递到SM中，或及时存储运算结果，GPU工作工作效率会大打折扣

## Slide 32: Optimization
Maximum CUDA Occupancy
  Occupancy = Max threads running / Max threads possible
Increasing the effective bandwidth
  Useful bytes delivered = average latency * bandwidth
    Coalescing global memory
    Use shared memory
    Minimum time waiting at barriers
Notes: 内存不能及时将数据传递到SM中，或及时存储运算结果，GPU工作工作效率会大打折扣

## Slide 33: ACTIVE EXPOSURE CONTROL WITH CUDA
Chart: Average Elapsed Time of Different Code Version per Frame
OpenCV CPU version | 24.72
OpenCV GPU version | 19.15
CUDA | 7.69
Notes: 预计18个月会将芯片的性能提高一倍。
Power=number of cores; Power = (frequency)3

## Slide 34: Question?